## Slide 1: XMASS
1. XMASS: physics targets
2. 3kg FV prototype detector
feasibility confirmation
3. 800kg liquid xenon detector
Search for dark matter
19th October 2006
ICRR external review meeting,
S. Moriyama, ICRR

## Slide 2: XMASS collaboration (2000-)
ICRR, Kamioka observatory:
Y. Suzuki, M. Nakahata, S.Moriyama, M. Shiozawa,
Y. Takeuchi, M. Miura,Y. Koshio, A.Takeda, K.Abe,
H.Sekiya, H.Ogawa, A.Minamino, T.Iida, K.Ueshima
ICRR, RCNN: T. Kajita, K. Kaneyuki
Saga Univ.: H. Ohsumi
Tokai Univ.: K. Nishijima, M.Sakurai, T.Maruyama
Gifu Univ.: S. Tasaka
Waseda Univ.: S. Suzuki, J. Kikuchi, T. Doke, A. Ohta, Y.Ebizuka, K.Deguchi
Yokohama Nat. Univ.: S. Nakamura, K. Uchida, M. Kikuchi, K. Tomita, Y. Ozaki, T. Nagase, T. Kamei, M. Shibasaki, S. Hagiawara
Miyagi Univ. of Edu.: Y. Fukuda, T. Sato
Nagoya Univ. : Y. Itow
Seoul National Univ.: Soo-Bong Kim
INR-Kiev, Ukraina: O. Ponkratenko,
UCI, USA: H. Sobel, M. Smy, M. Vagins, P.Cravens
Sejon University: Y.D.Kim, J.I.Lee, S.H.Moon
48 collaborators, 13 institutes

## Slide 3
1. XMASS: physics targets
Dark matter
Double beta
Solar neutrino
Xenon MASSive detector for solar neutrino (pp/7Be)
Xenon neutrino MASS detector (bb decay)
Xenon detector for Weakly Interacting MASSive Particles (DM search)
Goal: Multi purpose low-bg experiment with 10t LXe
LXe scintillator

## Slide 4: Ultimate sensitivity with 10t LXe: Direct detection of Dark Matter
Max.-sensitivity, <10-10pb for spin independent xsec (5yr)
Eth = 5keV: 2000 events/day
（Eth = 20keV: 30 events/day）
Large photosensitive area
CDMSII
DAMA
XMASS 10t
Ellis et al. post-LEP benchmark
10
102
103
WIMP mass (GeV)
10-10
10-8
10-6
10-4
xsec. to nucleon [pb]

## Slide 5: Why Liquid Xenon?
General properties:
Large scintillation yield (~42000photons/MeV ~NaI(Tl))
Scintillation wavelength (175nm, direct read out by PMTs)
Higher operation temperature (~165K, LNe~27K, LHe~4K)
Compact (r=2.9g, 10t detector ~ 1.5m cubic)
Not so expensive
Well-known EW xsec for solar n, 136Xe bb, large A (SI)
External gamma ray background:
Self shielding (large Z=54)
Internal background:
Purification (distillation, etc)
No long-life radio isotopes
Isotope separation is relatively easy
No 14C contamination (can measure low energy)
Circulation

## Slide 6: Key idea: self shielding effect for low energy signals
Large Z makes detectors very compact
Large photon yield (42 photon/keV ~ NaI(Tl))
Liquid Xe is the most promising material.
PMTs
Single phase
liquid Xe
Volume for shielding
Fiducial volume
23ton all volume (d=240cm)
20cm wall cut
30cm wall cut (10ton FV)
BG normalized by mass
1MeV
0
2MeV
3MeV
Large self-shield effect
External g ray from U/Th-chain

## Slide 7: Strategy of the XMASS project
800kg detector
(FV 100kg)
Dark matter search
~20 ton detector
(FV 10ton)
Solar neutrinos
Dark matter search
Prototype detector
(FV 3kg) R&D
~2.5m
~1m
~30cm
Feasibility confirmed
Confirmation of feasibility of the ~1ton detector
Double beta decay option?

## Slide 8: 2. 3kg FV prototype detector
In the
Kamioka Mine
(near the Super-K)
Liq. Xe
(31cm)3
MgF2 window
54 2-inch low BG PMTs
g ray/neutron shield
OFHC cubic chamber
Demonstration of reconstruction,
self shielding effect, and low background properties.
16% photo-
coverage
Hamamatsu
R8778

## Slide 9: Vertex and energy reconstruction
å
-
=
PMT
n
n
L
)
!
)
exp(
Log(
)
Log(
m
m
L: likelihood
m
:
F(x,y,z,i)
x total p.e.
S F(x,y,z,i)
n: observed number of
p.e
.
=== Background event sample ===
QADC, FADC, and hit timing
information are available for analysis
F(x,y,z,i): acceptance for i-th PMT (MC)
VUV photon characteristics:
Lemit=42ph/keV
tabs=100cm
tscat=30cm
Calculate PMT acceptances from various
vertices by Monte Carlo.
Vtx.: compare acceptance map F(x,y,z,i)
Ene.: calc. from obs. p.e. & total accept.
Reconstructed
here
FADC
Hit timing
QADC
Reconstruction is performed by
PMT charge pattern (not timing)

## Slide 10: Source run (g ray injection from collimators) I
DATA
MC
Collimator A
Collimator B
Collimator C
A
B
C
+
+
+
Well reproduced.

## Slide 11: Source run (g ray injection from collimators) II
Self shield works as expected.
Photo electron yield ~ 0.8p.e./keV for all volume
Gamma rays
Z= +15
Z= -15
137Cs: 662keV
DATA
MC
PMT
Saturation
region
-15
+15cm
-15
+15cm
~1/200
~1/10
Reconstructed Z
Reconstructed Z
Arbitrary Unit
10-1
10-2
10-3
10-4
10-5
10-1
10-2
10-3
10-4
10-5
60Co: 1.17&1.33MeV
DATA
MC
No energy
cut, only
saturation cut.
BG subtracted
r=2.884g/cc

## Slide 12: Background data
MC uses U/Th/K activity from PMTs, etc (meas. by HPGe).
Self shield effect can be clearly seen.
Very low background (10-2 /kg/day/keV@50-300 keV)
REAL DATA
MC simulation
All volume
20cm FV
10cm FV
(3kg)
All volume
20cm FV
10cm FV
(3kg)
10-2/kg/day/keV
3.9days livetime
Event rate (/kg/day/keV)
0
2000
1000
10-2
1
3000
keV
10-1
0
2000
1000
3000
keV
10-2
1
10-1

## Slide 13: Internal background activities
Current results
  238U(Bi/Po): = (33+-7)x10-14 g/g
  232Th(Bi/Po): < 23x10-14 g/g
  Kr: = 3.3±1.1ppt
Factor ~10 (under further study)
Achieved by distillation
Factor ~30, but may decay out further
Goal to look for DM by 800kg detector
1x10-14 g/g
2x10-14 g/g
1 ppt
x3
x12
x33
Very near to the target level of U, Th Radon and Kr contamination.

## Slide 14: Distillation to reduce Kr (1/1000 by 1 pass)
Very effective to reduce internal impurities (85Kr, etc.)
We have processed our Xe before the measurement.
 | Boiling point (@1 atm)
Xe | 165K
Kr | 120K
~3m
13 stage of
Operation: 2 atm
Processing speed: 0.6 kg / hour
Design factor: 1/1000 Kr / 1 pass
Lower temp.
Higher temp.
~1%
2cmf
~99%
Purified Xe:
=3.3±1.1ppt Kr (measured after
Kr-enrichment)
Off gas Xe:
330±100 ppb Kr
(measured)
Original Xe:
~3 ppb Kr

## Slide 15: 3. 800kg(100kg FV) detector for DM search
Improve Energy threshold  immerse PMTs into LXe
Ext. g BG: from PMT’s  Self-shield effect demonstrated
Int. BG: Kr (distillation), Radon  Almost achieved
“Full” photo-sensitive,“Spherical” geometry detector
80cm diameter
812-hex PMTs (1/10 Low BG)
70% photo-coverage ~5p.e./keVee
g ray BG from PMTs:
60cm, 346kg
40cm, 100kg
Achieved
pp & 7Be solar n
Expected dark matter signal
(assuming 10-42 cm2, Q.F.=0.2 50,100GeV)

## Slide 16: More detailed geometrical design
A tentative design (not final one)
12 pentagons / pentakisdodecahedron
This geometry has been coded in a Geant 4 based simulator
Hexagonal PMT
~50mm diameter
Aiming for 1/10 lower BG than R8778
R8778: U 1.8±0.2x10-2 Bq
Th 6.9±1.3x10-3 Bq
40K 1.4±0.2x10-1 Bq

## Slide 17: 800kg reconstruction and BG study energy threshold: 5keV (~25p.e.)
10keV
R=5cm
Extensive study to optimize the detector ongoing
5 keV
10 keV
50 keV
100 keV
500 keV
1 MeV
Fiducial volume
20
10
30
0
40
8
10
6
4
2
0
12
Distance from the center [cm]
s (reconstructed) [cm]
10keV
R=35cm
Photon tracking: absorption,
scattering, and reflection

## Slide 18: Expected sensitivity
Large improvements ~102 expected.
XMASS800kg
Edelweiss Al2O3
Tokyo LiF
Modane NaI
CRESST
UKDMC NaI
NAIAD
XMASS FV 0.5ton year (100kg, 5yr)
3s discovery
w/o any pulse shape information
10-6
10-4
10-8
10-10
Cross section to nucleon [pb]
10-2
1
102
104
106
Plots except for XMASS:
http://dmtools.berkeley.edu
Gaitskell & Mandic
SuperCDMS Phase A
XENON100
XMASS800kg
CDMSII
10
102
103
10
102
103
10-4
WIMP mass (GeV)
WIMP mass (GeV)
SI
SD
J Ellis et al. benchmark
WARP 140kg

## Slide 19: New experimental hall
15m
21m
15m
Water shield
XMASS
detector
Super-K
New
hall 1
Hall 2
New two halls will be excavated by the next summer.
One of them accommodates the xmass detector including a large water shield which protects it from gamma rays and neutrons.
250cm water
g ~10-4
Fast neutron ~ 10-5
8m
9m

## Slide 20: Summary
XMASS aims to detect
Low energy solar n, 0nbb decay, and Dark Matter
Feasibility for 800kg liquid xenon detector was confirmed with the prototype detector.
Reconstruction, self shielding, and purification tech. have been demonstrated.
800kg detector is under designing.
102 improvement of sensitivity (~10-9pb) above existing experiments is expected.