## Slide 1: Fast waveform digitizing for the search of the m+ → e+g decay
Stefan Ritt :: Paul Scherrer Institute :: Switzerland
ICRR Seminar, University of Tokyo, Chiba, March 31st, 2017

## Slide 2: Fast waveform digitizing for the search of the m+ → e+g decay
Stefan Ritt :: Paul Scherrer Institute :: Switzerland
ICRR Seminar, University of Tokyo, Chiba, March 31st, 2017
LHC

## Slide 3: Two talks in one
The “pure” science
Search for New Physics via charged lepton flavor violation (cLFV)
The “dirty” technology behind
Ultrafast waveform digitizing

## Slide 4: Motivation for cLFV searches
Standard Model (SM) of particle physics is very successful, but falls short on
  Dark matter
  Matter-antimatter asymmetry
  Gravity
  ...

## Slide 5: Searches for New Physics Beyond the SM
Real BSM
particles
Energy Frontier – LHC/ILC
“Direct” Searches L ~ 10 TeV
Virtual BSM
particles
Intensity Frontier - cLFV
“Indirect” Searches L > 1000 TeV

## Slide 6: Quick introduction to cLFV
Lepton Flavor Violation
  observed in the neutral sector (neutrino oscillations)
  Not observed in the charged sector “accidental” symmetry!
Neutral Sector
Charged Sector
νe
ντ
νµ
µ ➔ eɣ
µ ➔ eee
τ ➔ eɣ
…
✓
X

## Slide 7: cLFV in the SM
g
W-
m-
nm
ne
e-
g
m-
e-
“Beauty of cLFV”
cLFV is possible in the SM through neutrino mixing, but immeasurable small
⇒ A cLFV signal would be clear evidence for New Physics

## Slide 8: cLFV processes sensitive to New Physics (NP)
m, t “forbidden” decays
m  e
conversion
Anomalous
magnetic
moment

## Slide 9: History of cLFV searches with muons
Started with Pontecorvo & Hincks 1947
Currently all three limits held by PSI experiments
MEG II experiment aim for 10x improvement
COMET (JPARC) and Mu3e aim for > 100x improvement
1940 1950 1960 1970 1980 1990 2000 2010 2020 2030
10-1
10-2
10-3
10-4
10-5
10-6
10-7
10-9
10-10
10-11
10-12
10-13
10-14
10-15
10-16
10-8
10-17
1
m → e g
mA → eA
m → eee
MEG
MEGII
COMET
Mu3e
Mu2e
SINDRUM

## Slide 10: cLFV Experiments at PSI
Mu3e (Phase I+II)
µ+→e+e-e+
MEG / MEG II
µ+→e+ɣ
Sensitivity Goal
≈ 4 x10-14
Sensitivity Goal
≈ 1 x10-16
High Intensity Proton
Accelerator facility:
590 MeV proton energy
2.4 mA proton current
1.4 MW power

## Slide 11
The MEG Experiment

## Slide 12: MEG Experiment at PSI
～70 researchers from 5 countries

## Slide 13: Signal and Background m→ e g
Signal
qge = 180º e and g in time Ee = 52.8 MeV Eg = 52.8 MeV
e
g
m
180º
52.8 MeV
52.8 MeV
n
e
g
m
< 52.8 MeV
< 52.8 MeV
n
Prompt Background
n
e
g
m
< 52.8 MeV
n
n
m
n
e
Accidental Background
m→ e g

## Slide 14: MEG Experiment Layout
γ
μ+
e+
1m
Drift Chamber
Ultra-light material
Precise measurement
of e+ tracks
COBRA Magnet
Gradient field s.c. 1.27 T magnet
sweeps out “high pT” e+ quickly
Muon Beam
Most intense DC muon beam
up to 108 m/s on target
Timing Counter
Resolution <100ps
in 1.4T B-field
Liquid Xenon Calorimeter
World’s largest LXe calorimeter ~900 l (2.7t) with 846 PMTs
immersed in Xenon
Lots of pioneering work

## Slide 15: A few pictures
Stopping
Target
LXe calorimeter assembly

## Slide 16: Calorimeter Calibrations
LED
PMT Gain
Higher V with light att.
Can be repeated frequently
alpha
PMT QE & Att. L
Cold GXe LXe
Laser
Laser
(rough) relative timing calib.
< 2~3 nsec
Nickel g Generator
9 MeV Nickel γ-line
NaI
Polyethylene
0.25 cm Nickel plate
3 cm
20 cm
on
off
Illuminate Xe from the back
Source (Cf) transferred by comp air  on/off
Proton Acc
Li(p,)Be
LiF target at COBRA center
17.6MeV g
~daily calib.
Can be used also for initial setup
K
Bi
Tl
F
Li(p, 0) at 17.6 MeV
Li(p, 1) at 14.6 MeV
p- + p  p0 + n
p0  gg (55MeV, 83MeV)
p- + p  g + n (129MeV)
10 days to scan all volume precisely
LH2 target
g
e+
e-
e
g
n
m
n
Lower beam intensity < 107 to reduce pile-ups
A few days ~ 1 week to get enough statistics
MEG Detector
Standard
Calibrations
p0 gg
m radiative decay
Absolute calibration, long term stability, continuous monitoring

## Slide 17: Requirements DAQ
Amplitude (charge) resolution 0.1% for liquid Xenon calorimeter
Time resolution < 100 ps
Pile-up rejection < 10 ns
t
< 52.8 MeV
0.511 MeV
~100ns
100ns
Calorimeter Signals
Waveform digitizing > 1 GSPS necessary !

## Slide 18: Flash ADC solutions
8 bits – 3 GS/s – 1.9 W  24 Gbits/s
10 bits – 3 GS/s – 3.6 W  30 Gbits/s
12 bits – 3.6 GS/s – 3.9 W  43.2 Gbits/s
14 bits – 0.4 GS/s – 2.5 W  5.6 Gbits/s
1.8 GHz!
24x1.8 Gbits/s
Requires high-end FPGA
Complex board design
FPGA power
PX1500-4: 2 Channel 3 GS/s 8 bits
ADC12D1X00RB: 1 Channel 1.8 GS/s 12 bits
1-20 k€ / channel

## Slide 19
Switched Capacitor Array (SCA) Chips

## Slide 20: Switched Capacitor Arrays
Shift Register
Clock
IN
Out
Waveform
stored
Inverter “Domino” ring chain
0.2-2 ns
FADC
33 MHz
10-100 mW
“Time stretcher” GHz → MHz

## Slide 21: Time Stretch Ratio (TSR)
Clock
IN
Out
dts
dtd
Dead time =
Sampling Window ∙ TSR
(e.g. 100 ns ∙ 60 = 6 ms)
Typical values:
dts = 0.5 ns (2 GSPS)
dtd = 30 ns (33 MHz) → TSR = 60

## Slide 22: Timing resolution estimation
voltage noise Du
timing uncertainty Dt
signal height U
rise time tr
number of samples on slope
Simplified estimation!

## Slide 23: Achievable timing resolution
U | Du | fs | f3db | Dt
100 mV | 1 mV | 2 GSPS | 300 MHz | ∼10 ps
1 V | 1 mV | 2 GSPS | 300 MHz | 1 ps
1V | 1 mV | 10 GSPS | 3 GHz | 0.1 ps
today:
optimized SNR:
next generation:
includes detector noise in the frequency region of the rise time
D.A. Stricker-Shaver, S. Ritt, B.J. Pichler, “Novel Calibration Method for Switched Capacitor Arrays Enables Time Measurements with Sub-Picosecond Resolution”, IEEE Trans.Nucl.Sci. 61 (2014), 3607

## Slide 24: Switched Capacitor Arrays for Particle Physics
STRAW3
TARGET
LABRADOR3
AFTER
SAMPIC
SAM
E. Delagnes
D. Breton
CEA Saclay
DRS1
DRS2
DRS3
DRS4
G. Varner, Univ. of Hawaii
0.25 mm TSMC
Many chips for different projects (Belle, Anita, IceCube …)
0.35 mm AMS, 0.18 mm IBM
T2K TPC, Antares, Hess2, CTA
H. Frisch et al., Univ. Chicago
PSEC1 - PSEC4
0.13 mm IBM
Large Area Picosecond Photo-Detectors Project (LAPPD)
2002
2004
2007
2008
0.25 mm UMC
Universal chip for many applications
MEG experiment, MAGIC, Veritas, TOF-PET
SR
R. Dinapoli
PSI, Switzerland
www.psi.ch/drs
www.phys.hawaii.edu/~idlab/
matacq.free.fr
psec.uchicago.edu

## Slide 25: MEG Electronics 1999-2013
PMT
Active
Splitter
Trigger
DRS4
DAQ
HV
Trigger Bus
Clock distribution
Power
DRS4
5 GSPS / 12 bit
3000 Channels DRS4 (0.8 GSPS / 1.6 GSPS)
1000 Channels Trigger (100 MSPS)
5 Racks
Separated DAQ & Trigger & HV
VME based system
DRS4 piggy-back on general purpose FPGA board

## Slide 26: MEG on-line waveform display
template
fit
S848
PMTs
“virtual oscilloscope”
Liq. Xe
PMT
1.5m
g
m
Drawback: 400 TB data/year

## Slide 27: Pulse shape discrimination
g
a
m
g
a
m

## Slide 28: Template Fit
Determine “standard” PMT pulse by averaging over many events  “Template”
  Find hit in waveform
  Shift (“TDC”) and scale (“ADC”) template to hit
  Minimize c2
  Compare fit with waveform
  Repeat if above threshold
Store ADC & TDC values
pb Experiment
500 MHz sampling
www.southerninnovation.com
14 bit
60 MHz

## Slide 29: Other Applications
Gamma-ray astronomy
Magic
CTA
Antarctic Impulsive Transient Antenna
(ANITA)
320 ps
IceCube
(Antarctica)
Antares
(Mediterranean)
ToF PET (Siemens)

## Slide 30: Things you can buy
DRS4 chip (PSI)
32+2 channels
12 bit 5 GSPS
> 500 MHz analog BW
1024 sample points/chn.
110 ms dead time
MATACQ chip (CEA/IN2P3)
4 channels
14 bit 2 GSPS
300 MHz analog BW
2520 sample points/chn.
650 ms dead time
DRS4 Evaluation Board
4 channels
12 bit 5 GSPS
750 MHz analog BW
1024 sample points/chn.
500 events/sec over USB 2.0
SAM Chip (CEA/IN2PD)
2 channels
12 bit 3.2 GSPS
300 MHz analog BW
256 sample points/chn.
On-board spectroscopy

## Slide 31
The MEG Result

## Slide 32: Full MEG Dataset
Chart: 
| 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0
Series 1 | 60000000000000 | 110000000000000 | 230000000000000 | 280000000000000 | 210000000000000
3 x 1014
2 x 1014
1 x 1014
Muons Stopped on Target
5.7x10-13 (2013)
NEW double statistics
2.4x10-12 (2011)

## Slide 33: MEG data analysis
3 years of heavy analysis work intentionally left blank...

## Slide 34: Event distribution
90% signal efficiency cut (74% for Eg) for not displayed variables
Highest probability events differ in left and right plots.
1, 1.64 and 2s
contours on
signal PDF
No indication of signal excess
e
g
m
180º
52.8 MeV
52.8 MeV

## Slide 35: Final MEG Result
Signal PDF (upper limit magnified by 100)
Best fit: BR(m→eg) = -2.2 x 10-13, Upper Limit: BR(m→eg) ≦ 4.2 x 10-13
Nacc = 7739 ± 38
NRMD =625 ± 28
Best fit to Data

## Slide 36: MEG Impact
L. Calibbi et al.
Eur. Phys. J. C74 (2014) 1-20
MEG 2016
Antusch et al. JHEP 0611 (2006) 090
MEG 2016
Large parameter space for BSM models (SUSY) are already excluded by MEG

## Slide 37: MEG: a “cover” experiment
Final MEG paper
Polarization Paper

## Slide 38
The MEG II Experiment

## Slide 39: MEG II
Increase beam intensity 3x107 m/s → 7x107 m/s
Improve detector resolutions to suppress increased background
PMT → SiPMT (4000 channels, >1m2) expected 2x better resolutions
Pixelated timing count expected s = 35 ps vs. 105 ps
New cylindrical drift chamber efficiency 88% vs. 46% hit resolution 120 mm
MEG I

## Slide 40: A few recent pictures
Cylindrical Drift Chamber
Pixelated Timing Counter
Liquid Xenon Calorimeter

## Slide 41: MEG vs. MEG II electronics
MEG Experiment 1999-2013
Separated DAQ & Trigger
3000 Channels DRS4 (0.8 GSPS / 1.6 GSPS)
1000 Channels Trigger (100 MSPS)
5 Racks
PMT
Active
Splitter
Trigger
DRS4
DAQ
HV
Trigger Bus
Clock distribution
SiPM
TDAQ
MEG II Experiment 2015-
9000 Channels
Same rack space
  Avoid dead space between boards
  Combine DAQ & Trigger
  Integrate high voltage
Timing requirement
  O(10 ps) between any two channels
Power
?
DRS4
5 GSPS / 12 bit

## Slide 42: Crate Options
Feature | VME | ATCA | ???
Transfer speed O(100 MB/s) | ✔ | ✔ | ✔
Dual-Star Topology with Gbit links | ✗ | ✔ | ✔
Shelf management | ✗ | ✔ | ✔
Fast trigger distribution | ✗ | ✗ | ✔
Low-jitter precision clock O(ps) | ✗ | ✗ | ✔
200 V SiPM biasing | ✗ | ✗ | ✔
< 2000 € per crate including power | ✗ | ✗ | ✔

## Slide 43: Custom Design “WaveDAQ”
Standard 19” crate + custom backplane
Idea: Not only a solution for MEG II, but more general “crate standard”
Take the best ideas on the market and combine them
  Single 24 V backplane power
  “Dual Star“ Serial gigabit links
  Serial bus (SPI) for configuration
  Hot-swap functionality
  Trigger / Busy signals in backplane
  Low skew (<5 ps) clock
  SiPM HV 200 V
  Shelf management with Ethernet interface
    Power
    Temperature
    Fans control
    Board management
    Firmware upload
Data Concentrator Board (DCB)
Trigger Concentrator Board (TCB)

## Slide 44: Half Height Backplane
5.43 ps

## Slide 45: WaveDREAM Board (WDB)
Drs4 based REAdout Module
Spartan 6
80 MSPS
5 GSPS

## Slide 46: WaveDREAM2 HV
+/- 1mV
Ripple < 10 mV
Microblaze @
Spartan
~ 20 $US / channel

## Slide 47: One-crate system Trigger & DAQ
220 V
Gbit Ethernet
Up to 256 Channels
Detector

## Slide 48: MEG II System
Scaling up to 16k channels

## Slide 49: WaveDAQ status
Successful beam test with stable operation
Noise level of at 4 mV @ gain 100 x
Multi-crate tests successful
Full 9000 channel system finished by end of 2017
Beam Test
Trigger Test
4 Create Test

## Slide 50: Waveform display in browser with HTML5
http://midas.psi.ch/scope

## Slide 51: Remote Data Visualization
mongoose.h
mongoose.c
Hardware
driver
PC
Controller
FPGA with soft-core
AJAX
JavaScript
Canvas
Browser with HTML5
Internet
Web-Server

## Slide 52: Smartphone and Tablet

## Slide 53: Outlook: DRS5
250 nm UMC → 110 nm UMC
Fast sampling stage: 10 GSPS with analog bandwidth > 1.5 GHz
Secondary sampling stages:
  32 x N bins each, total 4096 bins
  Self-triggered
  Store segments for ~ms (global trigger)
  Simultaneous sampling and digitization (quasi dead-time free)
On-chip Wilkinson ADC with fast serial link output
Successful test of 10 GSPS sampling stage in 2015
Final chip not before 2019
Ideas partially implemented in SAMPIC chip arXiv:1604.02385
shift register
input
fast sampling stage
secondary sampling stage
. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

## Slide 54: Conclusions
Final MEG result BR(m→eg) ≦ 4.2 x 10-14 @ 90% C.L. has been published in 2016
Technical developments took much longer than anticipated (1999-2008)
If you design your tool in a more general way, it can be to the benefit of other groups