## Slide 1: Study of alpha backgrounds using flash ADC in the XMASS experiment
Feb. 22nd , 2013
ICRR, Suzuki-Lab.
M2 Osamu Takachio

## Slide 2: Contents
Dark matter
XMASS experiment
DAQ system
Study of alpha backgrounds using flash ADC

## Slide 3: Dark matter

## Slide 4: Dark matter
Observed value
Can be explained by optical observation
Can be explained by dark mater
  WIMP (Weakly Interactive Massive Particle)
    Super symmetry particle(超対称性粒子)
Candidate of dark matter
Gravitational lens
Bullet Cluster
WMAP
Composition of the universe
Dark energy
Dark matter
Ordinary matter (4%)
Notes: 暗黒物質は電磁波で観測できる通常のグッ質の5~6倍を占める未知の物質。

## Slide 5: XMASS experiment

## Slide 6: XMASS experiment is …
A versatile low background experiment using liquid xenon as a scintillator
Ongoing from October 2010 for the realization of direct detection of dark matter.
Was operated until May 2012, and searching of the dark matter and understanding of the detector was done.
PMT holder inserted 642 PMTs
PMT 10789-11
Total mass 835kg
Effective mass100kg
Diameter 80cm (LXe)
Water tank
OVC/IVC
Notes: 10m10mの水タンク内部にOVC、IVC。
IVCの中に液体Xeが入っている。
その中に642本のPMTが挿入された球形(実際には正12面体の各面をさらに5つの三角形で分割したペンタキスドデカヘドロンという構造)のPMTホルダーがある。

## Slide 7: DAQ systems

## Slide 8: DAQ system
Trigger is generated from ATM HITSUM
• PMTSUM
Analog sum of the ~12 PMT signals input to 1 FADC channel (yellow).
FADC can take 642 all the PMT signals using 60 channels.
Notes: PMT、ATM、FADCの簡単な説明。
トリガーの仕組みとPMTSUMについて詳しく。

## Slide 9: Study of alpha backgrounds using flash ADC in the XMASS experiment

## Slide 10: Motivation
  Using waveform information available from FADC, we may be able to discriminate alpha events and gamma events.
  We want to know how much alpha background exists in the detector.
  With the information about alpha events (energy, position etc…), we want to identify and estimate the quantity of the cause of the background.
  Then, we can move to the removal work of the causative substance from the detector, etc.

## Slide 11: Waveform discrimination
In case of liquid xenon, the signals have different waveforms between nucleus recoil and electron recoil.
Waveform discrimination
  Alphas OR gammas
    For identification of background.
    ~MeV region
  Dark matter OR gammas
    For selection of dark matter signals.
    ~10keV region
Alpha
Electron(Gamma)
τs = 4.2ns
τl = 22ns
τ = 45ns
Electron(207Bi), α particles (210Po, 252Cf) was placed in a stainless-steel vessel(6.4cm in diameter) filled with liquid xenon.
Notes: 電子による電離イオン対の密度は低いため一部のイオン対はすぐに再結合できず、45nsという長い減衰時間を持つ。
一方、アルファ線や重イオンに対しては電離イオン対の密度が高いため再結合までの時間が短い。

## Slide 12: Peak search
Peak search method
  Time window is 4us.
  Baseline is the average of the first 100 samples.
  Starting point is the crossing point of +20 ADC count.
  Ending point is the crossing point of +10 ADC count.
  Search next start point.
Waveform Example
(First peak)
(Second peak)
Get parameters of the peak
  Area
    Integrate between the starting point and ending point.
    1count~22.4eV according to Co57 detector center calibration
  Time constant (τ)
    Fit exponential function
    (peak+10ns to peak+150ns).
Notes: 幅を100nsの信号と仮定すると後述の変換係数を用いておよそ80pCの事象に対応する

## Slide 13: Time constant distribution
Co57 calibrated energy( )
Time constant( )
Gammas
1/30 of data from August 19th to September 3rd, 2011(13.7days)
The events over 150keV can be discriminated using 50ns criteria.
Alphas
Notes: 時定数の見積もりにはサチュレーションしたチャンネルを抜いた波形和にフィット。

## Slide 14: Estimation of the time constant
τα = 43.3ns
σ = 0.8ns
τγ = 68.7ns
σ = 2.7ns
Alphas
E>4MeV
35470events
Mean 43.3ns
Sigma 0.8ns
Gammas
1MeV<E<2MeV
842600events
Mean 68.7ns
Sigma 2.7ns
The reason of bigger time constant than reference value (τα = 22ns, τγ = 45ns).
• PMT response and margin of the cable length(~5ns)
• frequency character of PMTSUM(~10ns) • discrepancy btw. Boards etc…
Project each plot to time constant axis to get mean value and sigma of alpha and gamma events.
Alphas
Gammas
Notes: ガンマの選択領域の理由
→PMTコバールのCo60からのガンマ線とわかってるから。
(聞かれたら…)
右側の肩はプリアンプのサチュレーションのため。

## Slide 15: Energy spectrum of the alpha events
Po214
Po218
Rn222
Alpha events
(105,051events)
(88.3mcps)
Uranium chain
(Secular equilibrium in the
liquid xenon in our detector)
Notes:   Detector surface which attach to liquid xenon contaminate Ra226 and then blend into xenon.

## Slide 16
Selection of Po214 events
RPo214 = 7.33 ± 0.01(stat.) × 10-3Bq
Decay rate of the pure Po214 is
for estimation of the quantity

## Slide 17: Comparison between data and MC
Energy [keV]
Energy [keV]
Events/day/keV
Events/day/keV
Data (pure Po214) 7.33mBq
MC (Po214) 7.33mBq
Data (All alpha - Po214)
MC (Rn222+Po218) 7.33×2 mBq
Data and MC is similar spectrum.
Data and MC is similar spectrum.
MC is less than data.
Po214
Rn222
Po218

## Slide 18: Re-evaluation of the amount of the uranium chain
Here I assume Rn222, Po218 and Po214 com into secular equilibrium, I treat the discrepancy as a systematic error.
  Data 1720events/day(>4400keV)
  MC 1267events/day(>4400keV)
  Then each decay rate is,

## Slide 19: Light center is …
The way to identify the position of the events using 642 PMT’s light information.
Equations
XMASS detector
Where ?
?
?
Light quantity of channel n
X-coordinate of channel n
Y-coordinate of channel n
Z-coordinate of channel n

## Slide 20: Light center distribution of Po214 events
Light center (mm)
Energy (keV)
data
MC
9047
events
23848
events
Correspond to the surface of the detector
7.7(MeV) ÷ (6.0 ± 0.5(MeV)) = 1.28 ± 0.11
We get a conversion factor for estimateion of the energy of the surface events.
(Due to visual estimation of the energy, I set the error larger)
①
②
③
①
②
③
XMASS detector
This curve is due to PMT saturation.
Here for next analysis,
(Po214)
(Data)
Notes: サチュレーションの効果をわかりやすく説明。
赤丸の部分が検出器内側表面に対応するという結論にする。
※できれば確証となる資料をBack upスライドに用意しておきたい。

## Slide 21: A peak observed at “4MeV”
→ To check the position of the events in the detector, I made the light center distribution of all alphas.
Newly found peak by this analysis!

## Slide 22: All alphas light center distribution and peak of the “4MeV”
EMean = 3.92 ± 0.01(stat.)MeV
(3.92 ± 0.01)MeV × (1.28 ± 0.11)
= 5.02 ± 0.44MeV
• Alpha like
• Occur around the surface of the detector
• E = 5.02 ± 0.44 MeV
Pb210 of the uranium chain downstream may be contained within the surface of the detector!
Correspond to the surface of the detector
data
(Scale factor)

## Slide 23: What is causing this alpha background??
Surface materials
① Cu (face to center) ?
② Cu (Side) ?
③ Cu (Bottom) ?
④ Goretex ?
⑤ PMT aluminum ?
⑥ PMT rim ?
⑦ PMT window ?
MC
This make “4MeV” peak
From this result,
I made alpha events using MC at,
Cu surface
Goretex surface
Uranium in PMT aluminum
(1.8Bq fixed from other analysis)
&
？Bq
(existence are suggested from the other analysis)

## Slide 24
MC : Uranium alpha(1.8Bq) + Pb210 alpha(0.025Bq)
DATA : All alpha spectrum
From the best fit between data and MC,
I got this value.
Cu surface Pb210
Goretex surface Pb210
0.025±0.004Bq
We are planning to implement electrostatic polishing on Cu to remove Rn daughters and quality control against Rn to prevent it being mixed into again.

## Slide 25: Summary
We can discriminate alpha like events and gamma like events using 50ns time constant criteria for over 150keV events.
There are about 88.3mcps alphas background in total.
Of them, as for the high energy part Rn222,Po218,Po214 in radon chain are dominant.
  If we assume secular equilibrium, 7.33±0.01(stat.)±2.62(sys.)mBq
We can see a peak at 4MeV in the energy spectrum.
  I succeed to identify the cause as Pb210 attached to the surface of the anoxic copper used as a PMT holder.
  From comparison between data and MC, total amount of the surface Pb210 was estimated at 25±4mBq.
Now, we are already carrying out our refurbishment works.
  Electrostatic polishing on Cu to remove Rn daughters
  quality control against Rn.